## Slide 1: DSO Entity and ENTSO-E Public Webinar on Flexibility Needs Assessment Methodology 24 April 2025
Hubert Dupin, Co-convener, DSO Entity
Mario Sisinni, Co-convener, ENTSO-E
Mehtap Alper, Senior Coordinator, DSO Entity

## Slide 2: Opening: Agenda
Webinar Items | Indicative Time | Presenter
Introductory remarks | 14:00-14:10 | Moderator: Mehtap Alper, on behalf of DSO entity ENTSO-E Joint Task Force
Overview of Methodology & Scope | 14:10-14:15 | Hubert Dupin, Convenor-DSO Entity
Roles and responsibilities & National Implementation | 14:15-14:25 | Hubert Dupin, Convenor-DSO Entity
Data and analysis | 14:25-14:30 | Mario Sisinni, Convenor-ENTSO-E
System flexibility needs | 14:30-14:40 | Mario Sisinni, Convenor-ENTSO-E
DSO flexibility needs | 14:40-14:50 | Hubert Dupin, Convenor-DSO Entity
Fine-tuning and guiding criteria | 14:50-15:00 | Mario Sisinni, Convenor-ENTSO-E
Market barriers and contribution of digitalisation | 15:00-15:05 | Hubert Dupin & Mario Sisinni
Concluding remarks and Q&A session | 15:05-15:30 | Moderator: Mehtap Alper, on behalf of DSO entity ENTSO-E Joint Task Force

## Slide 3: Assesment of Flexibility Needs: What is it about? Legal Basis: New Provisions of EMDR (EU (2024)1747)
Para 3
Para 4
DSO Entity and ENTSO-E submit the Methodology to ACER (16 April 2025)
Para 6
Para 3
ACER review amend and/or approve the Methodology within 3 months of the receipt of the proposal of DSO Entity & ENTSO-E (16 July 2025)
DSOs & TSOs implement the methodology and provide data and analysis to the NRA and/or Designated Entity
Para 1& 2
Para 7
NRA or Designated Entity shall submit the reports to the EC and to ACER and shall publish them
DSO Entity & ENTSO-E develop a joint Methodology for Assesment of Flexibility Needs
No later than 12 months after ACER approves the Methodology, NRAs or Designated Entity prepare National Flexibility Needs Assessment Reports
Methodology Drafting, Review & Approval:
9+3 months (July 2024– July 2025)
Process based on Article 19e of Electricity Regulation
National Implementation: Assessment & Reporting
12 months (July 2025- July 2026)
EU Wide Assessment
12 months (July 2026-July 2027)
Within 12 months of receipt of the reports, ACER shall issue an EU wide Assessment Report :
recommendations on issues of cross-border relevance
recommendations on removing barriers to the entry of non-fossil flexibility resources.
EMDR
Art 19e

## Slide 4: The Flexibility Needs Assesment (FNA) report adresses 5 different issues regarding the estimated flexibility needs for a period of at least the next 5 to 10 years at national level
evaluate the different types of flexibility needs, at least on a seasonal, daily and hourly basis, to integrate electricity generated from renewable sources in the electricity system, inter alia, different assumptions in respect to electricity market prices, generation and demand;
consider the potential of non-fossil flexibility resources such as demand response and energy storage, including aggregation and interconnection, to fulfil the flexibility needs, both at transmission and distribution levels;
evaluate the barriers for flexibility in the market and propose relevant mitigation measures and incentives, including the removal of regulatory barriers and possible improvements to markets and system operation services or products;
evaluate the contribution of digitalisation of electricity transmission and distribution networks;
take into account sources of flexibility that are expected to be available in other Member States.
TSOs & DSOs data
TSOs to consider while performing (market simulation for system needs)
National Entity / Authority to assess
TSOs to consider while performing (market simulation for system needs)
National Entity / Authority to assess
EMDR
Art 19e
1
2
3
4
5

## Slide 5: Drafting Process & Stakeholder Engagement
Stakeholder Group
Drafting Team
Observer Members
Secretariat
ENTSO & DSO Entity established a joint Task Force in April 2024. The drafting Team is represented by 9 TSOs and 10 DSOs. Observer group composes of 20 TSOs and 22 DSOs

## Slide 6: Development of the Flexibility Needs Assessment Methodology – Project Timeline
Methodology Development
Jul
Aug
Sept
2025
2024
Q1
Q2
Q3
Q4
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
06/09
Online Workshop
Introductory Workshop
Methodology Finalisation
16/04
Submission to ACER
08/11-06/12
Public Consultation
Mandated deadline
Stakeholder interaction
04/10
Physical Workshop
13/11
Physical Workshop
04/03
Public Webinar
Public interaction
15/11
Public
webinar
Legend
Internal approval
Secretariat processes
24/04
Public Webinar
Today
4 dedicated Stakeholder Sessions
4 weeks of Public Consultation
3 public Webinars
DSO Entity & ENTSO-E Joint proposal for FNA Methodology submitted to ACER on 16 April 2024!
Public Consultation Responses are published!
Jul
ACER Process-3 months (16 April-16 July)
17/07 Methodology Approval & Publication

## Slide 7: Overview of the Methodology & Scope
Hubert Dupin
14:10-14:15

## Slide 8
Provides insight to policy makers and stakeholders to make flexible resources available in the future when forecasted flexibility needs will arise, ensuring technological neutrality and cost efficiency
Provides a high level analysis of the policies as drivers for flexibility needs
Introduces a complementary perspective for DSOs and TSOs to address and contribute to issues regarding the whole electricity system
For DSOs, synthesizes at national level the needs and vision of all different operators (zoom out from DNDP). The methodology is feasible in each country for all DSOs, considering their diversity (size, context, voltage level, planning methods…) and availability of data
Supplements DNDP and adequacy studies (ERAA/NRAA), without overruling associated processes and ensuring consistency and complementarity
The Flexibility Needs Assessment (FNA) Methodology addresses both Network Needs and System Needs, complementing existing studies and supporting policy makers in the definition of targets for flex resources
'DSOs and TSOs consider this Flexibility Needs Assessment methodology as a valuable and necessary opportunity to highlight the importance of flexibility for the energy transition, both at distribution and transmission level':​​
Flexibility Needs Assessment methodology (FNA) brings a New Approach
'Provides a joint DSO-TSO perspective, complementing system and network views.'
SYSTEM NEEDS - CROSS BORDER
can be fulfilled ANYWHERE "copper plate"
NETWORK NEEDS - LOCATIONAL
will EVENTUALLY arise SOMEWHERE
and must be fulfilled WHERE and WHEN they occur

## Slide 9
Governance, Scope & Data
Article 1. Subject matter and scope
System Needs
Article 8. System needs
General Provisions
Article 17. Guiding criteria
Network Needs & finetuning
Article 12. Principles to assess DSO network flexibility needs
Article 2. Definitions
Article 3. Roles and responsibilities
Article 4. National implementation
Article 5. Confidentiality obligations
Article 6. Data and analyses
Article 7. Needs covered
Article 9. System needs – RES integration
Article 10. System needs – Ramping Needs
Article 11. System needs – Short-term flexibility needs
Article 13. DSO network flexibility needs
Article 14. TSO network flexibility needs
Article 15. Unavailability of flexible resources due to grid prequalification and temporary limits
Article 16. Fine-tuning system needs with network needs
Article 18. Derogations
Article 19. Amendments of the methodology
Article 20. Language
Article 21. Market Barriers and contribution of digitalisation
ANNEXES
Annex I - Examples of Table 1 to report DSO flexibility network needs
Annex II - Input data to FNA process – Type and format
Annex III - Possible topics for market barriers assessment
Overview of FNA Methodology

## Slide 10: Main Scope & Definitions
Other New Terms | Definition
RES Integration Needs | “quantity of flexibility required to achieve annual RES integration targets or maximum acceptable level RES curtailment for the Member State”
Ramping Needs | “needs associated with variations of the residual load assuming perfect forecast conditions”
Short-term Flexibility Needs | “needs associated with unexpected variations of the residual load or forced outage of assets during the intra-day or balancing timeframe”
‘upward (resp. downward) network flexibility needs’ | "means needs whose solution requires increasing (resp. decreasing) injection on the network or decreasing (resp. increasing) demand from the network"
ART 02
"The methodology covers DSO Flexibility Network Needs, TSO network needs and System needs"
SYSTEM FLEXIBILITY NEEDS
NETWORK FLEXIBILITY NEEDS
Definition: flexibility needed to adjust for grid availability, by means of preventing or solving congestion or voltage issues
Assessed by DSO and TSO in their grids
  Definition: flexibility needed by electricity system to adjust to variability of generation and consumption: RES integration needs, ramping needs, short-term flexibility needs
  Assessed by TSO, but associated to the whole electricity system
Notes: Hubert

## Slide 11: Roles and responsibilities & National Implementation
Hubert Dupin

## Slide 12: Art. 3-4 – Roles & Responsibilities and National implementation
17 July 2025
Approval of the FNA methodology ACER
Member State defines the Designated Entity or Authority responsible for the adoption of the report.
By the approval
of Methodology
by ACER
Member States
  Roles, responsibilities and timeline  may involve delegation for DSOs
  Justification of the use of material in addition to DNDP
  Common target years to provide data and analyses, in addition to the target years;
  Temporal, spatial and voltage granularity of DSOs data;
  Additional type of data and analyses, if any, beyond the minimum requirements of the methodology
  Timeframe for the approval of the FNA report
17 Oct 2025
Within 3 months after the approval
DSOs & TSOs
17 Nov 2025
Within 4 months after the approval
Designated Entity or Authority
TSOs and DSos
17 May 2026
Within 10 months after the approval
DSOs & TSOs
16 July 2026
Within 12 months after the approval
Designated Entity or Authority, TSOs and DSOs
  Designated Entity or Authority can request additional information beyond data and analysis required from TSOs and DSOs with this methodology.
  Request shall be justified and proportionate, and agreed by TSOs and DSOs (to the extent they are concerned)
Send data and analyses to the Designated Entity or Authority.
  Designated Entity or Authority consolidates and adopts the National FNA report.
  DSOs/TSOs who provided data / analysis coordinate with the designated entity to ensure clarity and correct representation of the provided data and analyses in the report
START
Process rerun every two years with the same timeframe
ART 03- 04

## Slide 13: National implementation
Synthesis of final article
TSOs and DSOs need sufficient to define at national level
  the organisation to process and deliver (can be > 100 DSOs in a country)
  The common target years
  the temporal, spatial and voltage granularity of DSOs data,
  then to perform analysis and provide data
Providing such data requires to adjust/create methods
Request for more time for national entity/authority
Insert a public consultation
Schedule too fast for TSOs/DSOs to provide new data (beyond existing methology)
Request to have different schedule for TSO vs DSOs
Upper boundary set at 10 months for TSOs & DSOs to provide data and analysis
Timeline to be coordinated at national level between TSOs/DSOs, National Entity/Authority and NRA
No timeframe set in EMDR for NRA to send data to ACER
Public consultation not foreseen
ART 03 - 05
Notes: Hubert

## Slide 14: Data & Analysis
Mario Sisinni

## Slide 15: Overview of data inputs & needs covered
Final approach
INPUTS
OUTPUT
European Resource Adequacy Assessment (ERAA) or
National Resource Adequacy Assessment (NRAA)
Other sources (for forecast error data, RES share target,...)
Distribution Network Development Plans and Other studies
System needs
(Arts 8 – 11)
RES integration, ramping needs, short-term needs including fine-tuning (Art 15)
Distrib. Netw. Flex Needs
(Arts 12-13)
Transm. Netw. Flex Needs
(Arts 14)
Information published for market-based procurement of local services (cf NCDR)
Unavailability of flexible resources
(Arts 16)
Annual national report on Grid Prequalification and Temporary limits (NCDR)
Guiding criteria
(Art 17)
Note: Number of articles correspond to the submitted document, but might slightly change in the final release
Art 8/Annex II
Art 16
Annex I
ART 06 - 07
Notes: MS

## Slide 16: Overview of data inputs & needs covered – ERAA -> FNA
ERAA input
NRAA input
And other national input
ERAA output
NRAA output
Separate economic dispatch
Flex needs
Same scenario
Consistent & unique set/format of input
Other national input (forecast error)
Consistent & unique set/format of output
Flex needs
Flex needs
Processing
Processing
Analysis
TSOs can choose among the use of ERAA or FNAA outputs to be processed to quantify flexibility needs or can rely on separate economic dispatch simulation using ERAA/FNAA input
The approach chosen by each TSO does not impact consistency of results and establishment of a European view.
ART 08
Notes: MS

## Slide 17: System Flexibility Needs
Mario Sisinni

## Slide 18: Overview of System Needs
Short-term flexibility needs (Art 11)
Quantify flexibility shortages associated to the management of up- and downward residual load / generation prediction errors based on the margins on dispatched units (ERAA / NRAA)
Ramping needs (Art 10)
Quantify flexibility shortages associated to the management of up- and downward residual load ramps over a period of 60 minutes or lower based on the margins of dispatched units (ERAA / NRAA) considering their technical constraints (e.g. ramping constraints)
RES integration needs (Art 9)
Study downward flexibility needs based on behavior of the ERAA/NRAA RES generation curtailment and residual load indicators
Characterize flexibility needs into different timeframes (daily, weekly, seasonal)
Quantify additional capacity of technology-neutral flexible resources to cover RES integration needs (i.e. RES integration targets)
System needs indicators
ART 08-11
Chart: 
0
Hours
Hours
RES curtailment
GW
GW
To meet RES integration targets a certain amount of curtailed RES generation has to be integrated through flexibility
RES Curtailed electricity
RES integrated electricity

## Slide 19: Overview of System Needs
Short-term flexibility needs (Art 11)
Quantify flexibility shortages associated to the management of up- and downward residual load / generation prediction errors based on the margins on dispatched units (ERAA / NRAA)
Ramping needs (Art 10)
Quantify flexibility shortages associated to the management of up- and downward residual load ramps over a period of 60 minutes or lower based on the margins of dispatched units (ERAA / NRAA) considering their technical constraints (e.g. ramping constraints)
RES integration needs (Art 9)
Study downward flexibility needs based on behavior of the ERAA/NRAA RES generation curtailment and residual load indicators
Characterize flexibility needs into different timeframes (daily, weekly, seasonal)
Quantify additional capacity of technology-neutral flexible resources to cover RES integration needs (i.e. RES integration targets)
System needs indicators
ART 08-11
Day-ahead Market Dispatch (Perfect forecast)
H1 (forecast)
H2 (forecast)
Residual load (GW)
Required RL ramp
Actual ramp-up capability
Gap

## Slide 20: Overview of System Needs
Short-term flexibility needs (Art 11)
Quantify flexibility shortages associated to the management of up- and downward residual load / generation prediction errors based on the margins on dispatched units (ERAA / NRAA)
Ramping needs (Art 10)
Quantify flexibility shortages associated to the management of up- and downward residual load ramps over a period of 60 minutes or lower based on the margins of dispatched units (ERAA / NRAA) considering their technical constraints (e.g. ramping constraints)
RES integration needs (Art 9)
Study downward flexibility needs based on behavior of the ERAA/NRAA RES generation curtailment and residual load indicators
Characterize flexibility needs into different timeframes (daily, weekly, seasonal)
Quantify additional capacity of technology-neutral flexible resources to cover RES integration needs (i.e. RES integration targets)
System needs indicators
ART 08-11
RL
H2 (actual)
H1 (forecast)
Intraday - Forecast error
H2 (forecast)
Required RL ramp
Actual ramp-up capability
Gap

## Slide 21: Overview of Transmission network needs
Upward transmission network needs (Art 14)
Correspond to energy not delivered due to transmission network constraints, which are not accounted in copper plate view
Downward transmission network needs (Art 14)
Correspond to generation curtailment due to transmission network constraints, which are not accounted in copper plate view
Network needs indicators
Optionally assessed by TSOs and then used to fine-tune RES integration system needs (Art 15)
Optionally assessed by TSOs to address conditions that are not observed from a system perspective
ART 14

## Slide 22: DSO Flexibility Needs
Hubert Dupin

## Slide 23: Distribution Network Flexibility Needs
Scenarios
Planning Methods
  DNDP shall provide data about flexibility needs (Art 32 ED)
  DNDP is a sound basis for DSO flexibility needs, consulted with all stakeholders, and NRA
DSOS with DNDP
Network planning methods
Characteristics at national and DSO level, including a distinction between voltage level and/or region
Is coordinated with the planning methodology and the scenario building process of the national TSOs for the TYNDP
Scenario and assumptions
Scenario and assumptions used to identify network development projects and local services needs
Considers available grid capacity for connection of new system users
Considers local services
Coordination between concerned DSOs and TSOs
encompass existing and future demand, generation, storage capacities, consider national energy and climate plans,
Description how local services are considered
Information on future evolution of the grid
Information on planned and ongoing investments for the next five to ten years
Consistency with National Energy Climate Plan, set the same targets for TSO and DSO at national level (2030)
DNDP provides a solid framework and is basis for the methodology
If DNDP is insufficient or unavailable, other methods can be used and must match DNDP
  Other Data sources such as market information for procurement of local services & supplementary methods / studies (If and as needed)
ART 12
Art 12
DNDP delivers an outlook for Local Flexibility for DSO’s, to be used as main input to the Methodology, supplemented by other sources

## Slide 24: DSOs shall deliver 5 types of data and analysis
The DSO network’s flexibility needs
“Table 2”  What we need
To prevent or solve congestion or voltage issue through active power
Reasoning for the DSO Network flexibility needs  Why we need it
Traceability  How the data is computed
Contribution to fine-tune system needs (adequacy assessments assessed by TSOs
Guiding criteria for distribution network flexibility needs being solved by local services  Which resources can cover our needs
How to assess the capability of the different sources of flexibility to cover the flexibility needs
including the potential effects of existing or planned frameworks and incentives to connect additional assets
Source of Data
Methods
Scenarios
If available, information on the expected contractual means to access flexibility
Maximum hourly volumes of flexible resources that could be limited under the national implementation of grid prequalification and temporary limits processes
DSO network needs (to the extent they do not overlap system needs of TSO network needs) - TSO to assess based on "Table 2" data
ART 13, 15, 16, 17

## Slide 25: Illustrative example (not real data) of Table 2
Yearly value – minimum data set
Direction | Target Year | Time block | Spatial granularity | Voltage level of congestion issue | Type of value | Flexibility network needs
Downwards needs flexibility | 2030 | Entire year | Bidding zone = Region 1 + Region 2 | High Voltage 132kV network | Total energy over the year | 4 500 MWh
 |  |  |  |  | Summ. Maximum power | 110 MW
 |  |  |  | Medium Voltage 20kV network | Total energy over the year | 2 000 MWh
 |  |  |  |  | Summ. Maximum power | 45 MW
Upwards needs flexibility |  | Entire year | Bidding zone Region 1 + Region 2 | High Voltage 132kV network | No need | 
 |  | Oct-March Mon-Sun 00:00-23:59 |  | Medium Voltage 20kV network | Total energy over the year | 60 MWh
 |  |  |  |  | Summ. Maximum power | 5 MW
Annex I

## Slide 26: Illustrative example (not real data) of Table 2
By region and time block
Direction | Target Year | Time block | Spatial granularity | Voltage level of congestion issue | Type of value | Flexibility network needs | Reasoning to define the time block
Downwards needs flexibility | 2030 | Jan-Dec Mon-Sun 00:00 - 23:59 | Region 1 | HV - 132kV network | Total energy over the entire time block | 3 000 MWh | RES generation in region 1 is 90% wind, 10 % PV
 |  |  |  |  | Summ. Max power | 50 MW | 
 |  |  |  | MV- 20kV network | Total energy over the entire time block | 1 500 MWh | 
 |  |  |  |  | Summ. Max power | 20 MW | 
Downwards needs flexibility |  | Apr-Oct Mon-Sun 12:00-16:59 | Region 2 | HV- 132kV network | Total energy over the entire time block | 1 500 MWh | RES generation in region 2 is 95 % PV
 |  |  |  |  | Summ. Max power | 60 MW | 
 |  |  |  | MV- 20kV network | Total energy over the entire time block | 500 MWh | 
 |  |  |  |  | Summ. Max power | 25 MW | 
Upwards needs flexibility |  | Any time |  | HV -132kV network | No Need |  | 
 |  | Oct-March Mon-Fri 19:00-07:59 and Sat-Sun 00:00-23:59 | Bidding zone Region 1 + Region 2 | MV- 20kV network | Total energy over the entire time block | 10 MWh | Off hours in winter
 |  |  |  |  | Summ. Maxi power | 3 MW | 
 |  | Oct-March Mon-Fri 08:00-18:59 |  |  | Total energy over the entire time block | 50 MWh | Working hours in winter
 |  |  |  |  | Summ. Max power | 5 MW | 
Annex I

## Slide 27: Illustrative example (not real data) of Table 2
Representative day (only used for fine tuning system needs)
Direction | Target Year | Time block | Spatial granularity | Voltage level of congestion issue | Type of value | Flexibility network needs | Reasoning to define the representative day
Downwards needs flexibility | 2030 | Jan-Dec Mon-Sun 00:00 - 23:59 | Region 1 | High Voltage 132kV network | Total energy during the representative day | 70 MWh | Typical windy day 90% wind, 10 % PV
 |  |  |  |  | Summ. Max power | 40 MW | 
 |  |  |  | Medium Voltage 20kV network | Total energy during the representative day | 30 MWh | 
 |  |  |  |  | Summ. Max power | 15 MW | 
Downwards needs flexibility | 2030 | Apr-Oct Mon-Sun 09:00-18:59 | Region 2 | High Voltage 132kV network | Total energy during the representative day | 30 MWh | Typical sunny day in a region 95 % PV
 |  |  |  |  | Summ. Max power | 50 MW | 
 |  |  |  | Medium Voltage 20kV network | Total energy during the representative day | 10 MWh | 
 |  |  |  |  | Summ. Max power | 20 MW | 
Upwards needs flexibility | 2030 | Any time |  | High Voltage 132kV network | No need |  | 
 |  | Oct-March Mon-Sun 0:00-23:59 | Bidding zone Region 1 + Region 2 | Medium Voltage 20kV network | Total energy during the representative day | 10 MWh | 2 hr local duration if/where needed
 |  |  |  |  | Summ. Max power | 5 MW | 
A representative day is
a repetitive situation within a time block;
a particular situation, relevant for network development or operations, such as extreme situations
Annex I

## Slide 28: Finetuning & Guiding Criteria
Mario Sisinni
14:40-14:50

## Slide 29: Fine-tuning of system needs with DSO & TSO network needs + unavailability of resources
System needs (T+D)
T
D
D
T
D
Local Transmission Network need 1
Local Distribution Network need 1
Total flexibility needs of the power system include both system needs and local network needs.
The quantification of system needs is carried out at bidding zone level, considering copper plate conditions. As such it does include system needs occurring both at transmission and distribution level, although not specifically localizing them. These can be covered through resources located anywhere.
Transmission and Distribution Network needs occurs locally and can be solved only through local resources.
-> Simply summing up system and network needs is not a correct operation, for it could result in double-counting
Local Distribution Network need 2
TOTAL FLEXIBILITY NEEDS
The approach considered in the methodology provides for fine-tuning of system needs by reflecting network needs on system needs. This is applied to the RES integration need.
All system needs are also fine-tuned considering the unavailability of flexible resources due to pre-qualification & temporary limits.
ART 15 and 16

## Slide 30: Fine-tuning of RES integration need (Art 9)
Final Approach
Chart: RES curtailment - System need only
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 2 | 4 | 0 | 2 | 6 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: RES curtailment – Trans. network need
 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 1 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0
Chart: RES curtailment - Distribution network need
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.5 | 0.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Time-series derived from transmission network simulation, pursuant to Art 14 of the methodology
Data provided by DSOs and converted into hourly time-series by TSOs, pursuant to Art 15 of the methodology (see next slide)
Time series used for assessment of RES integration needs, without finetuning pursuant to Art 9 of the methodology
Chart: RES curtailment – System need + network needs
 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 1 | 3 | 2 | 4 | 0 | 2 | 6 | 4 | 0 | 0.5 | 0 | 2 | 0 | 0 | 0 | 0 | 0
Time-series used for assessment of fine-tuned RES integration needs, pursuant to Art 9 of the methodology
For each hour we take the max RES curtailment among system need only, transmission network need and distribution network need
Both sets of RES curtailment time series have to used to quantify RES integration flexibility needs.
Fine-tuning is only done when conditions of Art 15. applies
Analysis carried out at BZ level

## Slide 31: Guiding criteria for DSO
What is the purpose of Guiding Criteria?
To assess the capability of different flexibility resources to cover the flexibility needs
Why do we need?
To provide information to have enough resources to cover our needs
Main source of data:
Market information published for the procurement of local services (cf NCDR), which provides the finest possible locational granularity and technical specifications
Guiding criteria include the following technical indicators:
the location of the flexibility need;
the direction of activation (upwards or downwards);
the timeframe in which the resource shall be available to solve the flexibility need;
the local maximum power required during the activation;
if available, data related to the forecasted use, such as:
  the duration of a continuous need;
  the cumulated duration of discontinuous need per time block;
  a measure of the frequency of activation (level of recurrence or sporadicity);
  a cumulated energy per time block;
the applicable economic criteria;
other available relevant criteria.
DSO network needs can appear or increase rapidly at any given location.
For DSOs, capability to access needed resources in a timely manner at each needed location is critical and permanent.
Advocacy for this overarching principle will be done out of this method.
Final approach
ART 17

## Slide 32: Guiding criteria for TSOs
Final Approach
Chart: Flex capacity (GWh)
| 0 | 2 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1750 | 2000 | 2500 | 3000
Daily - 1h | 30239.2981 | 29678.4649 | 28852.5619 | 27510.2719 | 24958.3165 | 22527.5721 | 20201.3296 | 17989.788 | 15906.9714 | 13983.0551 | 12193.6241 | 10532.7293 | 9007.907 | 3513.5117 | 797.9144 | 105.2367 | 33.8759 | 0
Daily - 4h | 30239.2981 | 29709.1704 | 28918.3849 | 27614.6053 | 25075.1131 | 22630.3915 | 20299.8988 | 18098.5094 | 16025.1965 | 14068.8799 | 12262.4857 | 10575.7339 | 9033.97 | 3513.5117 | 797.9144 | 105.2367 | 33.8759 | 0
Weekly - 20h | 30239.2981 | 30103.7439 | 29901.3455 | 29565.7268 | 28898.8413 | 28237.8137 | 27583.479 | 26937.9198 | 26299.0577 | 25668.0581 | 25045.764 | 24428.5003 | 23818.8753 | 20906.5854 | 18190.2239 | 15666.3233 | 13341.5791 | 11218.1957 | 9337.2893 | 7663.2889 | 6195.4779 | 3945.5401 | 2410.7136 | 1487.8085 | 1169.6911 | 1056.4191 | 1227.5648
Weekly - 50h | 30239.2981 | 30181.5114 | 30095.0533 | 29951.401 | 29665.3771 | 29380.6938 | 29096.9912 | 28814.5827 | 28533.287 | 28252.9544 | 27973.1865 | 27694.9078 | 27417.5258 | 26050.0255 | 24713.3264 | 23402.3325 | 22121.6938 | 20879.4236 | 19667.5236 | 18483.2626 | 17326.7094 | 15104.7492 | 12989.541 | 11022.4123 | 9336.3295 | 7843.7677 | 6498.1006 | 5314.1227 | 4274.6841 | 3391.2112 | 2629.3901 | 1216.673 | 386.7248
Annual - 50h | 30239.2981 | 30214.9721 | 30178.5107 | 30117.814 | 29996.7865 | 29876.0831 | 29755.6065 | 29635.5062 | 29515.5737 | 29396.0016 | 29276.6395 | 29157.5646 | 29038.6576 | 28447.6857 | 27864.5938 | 27290.8824 | 26724.0633 | 26165.4456 | 25614.7256 | 25072.2759 | 24537.9399 | 23493.5859 | 22487.6717 | 21516.2802 | 20581.1706 | 19687.1277 | 18828.9969 | 18011.44 | 17230.3268 | 16487.1483 | 15780.8116 | 14175.726 | 12791.7712 | 10570.3239 | 9052.4608
The proposed approach aims at providing additional information to the policymaker, derived from the implementation of Art. 9-10-11, 15 of the methodology, such as:
Sub-indicators clarifying technical requirements associated to the needs related to frequency, volumes, duration, etc.
Contribution of the various types of additional flex capacity to reducing needs (e.g. to reducing RES curtailment in the image on the left)
Approaches to take into account also cost information (CAPEX and OPEX of technologies), to be possibly implemented beyond the FNA scope
4h
8h
20h
50h
ART 17

## Slide 33: Market Barriers and contribution of digitalisation
ART 21 & Annex III
'....NRAs or the designated authority or entity is responsible for analysing market barriers and the contribution of digitalisation to be included in the FNA report,'
'...and may rely on information provided in Annex III by relevant national entities; if an authority or entity other than the NRA is designated to prepare the FNA report, it may request and coordinate contributions from other relevant entities, including the NRA, to carry out this assessment.'
Pursuant to Article 19e of the Electricity Regulation:
Requirements to provide balancing services
Pre-qualification of reserve providing groups
Design of balancing products and market architecture
Market access to new entrants and small actors
Participation in different timeframes and product markets, possibly split by technology, or by aggregation model
Network charges for active customers
Requirements to provide congestion management
Administrative and infrastructure barriers
Incentives to provide flexibility
Smart meters and submeters roll-out
Availability of Time-of-Use network tariffs
Availability of time-differentiated retail electricity contracts and dynamic electricity price contracts
Consumer awareness and engagement
Annex III: Possible topics for market barriers assessment (Only for recommendation)

## Slide 34: Conclusion
The proposal was submitted to ACER on 16 April.